## Slide 1: Linux meets robotics

## Slide 2: Have you ever seen automated restaurants?

## Slide 5: How do they work?

## Slide 6: Raspberry pi 5

## Slide 7: Initial concept.

## Slide 8: Two pillars that keep the bot alive.
IPC
mq_send(mq, &order_msg, sizeof(order_msg), 0);
The ordering UI and the balancing arm run as independent Linux processes. They communicate via a POSIX message queue (/dev/mqueue). When an order is placed, a structured message is pushed onto the queue — the arm process reads it and adjusts grip stance before movement begins. No shared memory, no race conditions on the data path.
SCHED
sched_setscheduler(pid, SCHED_FIFO, &sp);
The balancing loop is promoted to real-time scheduling class SCHED_FIFO with the highest priority. The ordering UI runs at default nice value (0). Linux's CFS ensures the balance loop pre-empts the UI if both are runnable — a spill prevention measure at the OS level.

## Slide 9: 01 Pathing & Sensor System
Specs
Ultrasonic + IR sensor array for obstacle detection
PID-controlled motor drivers for smooth navigation
Linux kernel handles real-time GPIO via /sys/class
Dedicated OS process at elevated niceness priority
Code:

## Slide 10: 02 Smart Balancing Arm
Specs
IMU sensor (MPU-6050) samples orientation at 100 Hz
Servo correction loop runs as a high-priority process
Keeps drinks & food level regardless of bot motion
Communicates via POSIX message queue (IPC) with order system
Code:

## Slide 11: Issues faced
Race Condition: Sensor Write vs. Arm Read
CPU Scheduling Conflict: UI Starving the Balance Loop
GPIO Timing Jitter on Pi 4 (Resolved by Upgrade)

## Slide 12: What’s next?

## Slide 13: THANK YOU.